# SCPI commands scheduled for upcoming releases

Please note that the following list is preliminary.

SCPI command	Description
DCL	Requires the client (controller) to send a "DCL\n" string
*SRE	Sets the value of the Service Request Enable register
*WAI	Waits until all pending commands are completed
CALibration
:TEMPerature
[:DATA] {<new value>}	Enters the calibration value
INSTrument
:COUPle
:TRIGger {<mode>}	Selects a coupling between channels trigger systems
OUTPut
:DELay
:ON {<time>}	Sets the delay time for turning the output on
:OFF {<time>}	Sets the delay time for turning the output off
:DPRog {<bool>}	Controls down-programmer circuit
[SOURce[<n>]]
:CURRent
:SLEW
:FALLing	Sets the falling current slew rate
:RISing	Sets the rising current slew rate
:VOLTage
:SLEW
:FALLing	Sets the falling voltage slew rate
:RISing	Sets the rising voltage slew rate
SYSTem
:COMMunicate
:ETHernet	Ethernet communication parameters
:CONTrol?	Queries communication port for SRQ handling
:HOSTname {<name>}	Sets the Ethernet communication host name
:DIGital
:TOUTput
:BUS[:ENABle] {<Bool>}	Enables/disables BUS-generated triggers on digital pins
:ERRor
:ALL?	Queries the error/event queue for all the unread items
:CODE[:NEXT]?	Queries the error/event queue for the next item code
:TIME
:TIMer
[:STATe]	Sets the internal timer state
:COUNt	Queries the current value of the internal timer