# SCPI commands scheduled for upcoming releases

Please note that the following list is preliminary.

SCPI command	Description
DCL	Requires the client (controller) to send a "DCL\n" string
*SRE	Sets the value of the Service Request Enable register
*WAI	Waits until all pending commands are completed
CALibration
:TEMPerature
[:DATA] {<new value>}	Enters the calibration value
DISPlay
:CMAP {<palette>}	Sets color palette (theme)
:CMAP:COLor:CATalog?	Returns names and RGB values of all available colors
:CMAP:COLor[:RGB] {<name>, <red>, <green>, <blue>}	Sets RGB value for the selected color
INSTrument
:COUPle
:TRIGger {<mode>}	Selects a coupling between channels trigger systems
MMEMory
:CLOSe	Closes the file specified in NAME
:FEED	Sets data handle used to feed data into the file
:NAME {<filename>}	Sets the file name ro be opened or closed
:OPEN	Opens the file specified in NAME
OUTPut
:PROTection
:MEASure {<bool>}	Enables measuring of output voltage before channel output is turned on
SENSe
:AHOur
:RESet {<channel>}	Resets the amp-hour (Ah) measurement to zero
:WHOur
:RESet {<channel>}	Resets the watt-hour (Wh) measurement to zero
[SOURce[<n>]]
:ARB
:AMPlitude {<amplitude>}	Sets the arbitrary waveform amplitude
:COUNt {<count>}	Sets the number of arbitrary waveforms
:FREQuency {<frequency>}	Sets the arbitrary waveform frequency
:FUNCtion {<type>}	Sets the arbitrary waveform parameter type
:OFFset {<level>}	Sets the offset level of the arbitrary waveform
:PHASe[:ADJust] {<angle>}	Set the arbitrary waveform start phase
:SHAPe {<waveform>}	Selects the shape of the arbitrary waveform
SYSTem
:CHANnel
:INFOrmation
:AHOur
TOTal?	Returns channel’s total delivered energy in Ah
:WHOur
TOTal?	Returns channel’s total delivered energy in Wh
:COMMunicate
:ETHernet
:CONTrol?	Queries communication port for SRQ handling
:DIGital
:TOUTput
:BUS[:ENABle] {<Bool>}	Enables/disables BUS-generated triggers on digital pins
:ERRor
:ALL?	Queries the error/event queue for all the unread items
:CODE[:NEXT]?	Queries the error/event queue for the next item code
:KEY
:DEFine {<key>, <block>}	Sets the definition of the key
:DELete {<key>}	Removes the definition of the key
:TIME
:TIMer
[:STATe]	Sets the internal timer state
:COUNt	Queries the current value of the internal timer